ACCELERATOR DESIGN WORKSHOP (TOPIC III)

Context: MADX - Design of a circular electron- positron collider for the production of the tt pair. Required parameters:

2.- DESIGN OF A BASIC ARC CELL

a) Lattice choice: FODO Cell
A very high energy of the electrons is required because the top quark is so energetic. This means that electrons will have a very big momentum and so a strong beam rigidity is needed. In this sense, the lattice design that is the most optimized for dipole implementation is FODO since it only requires one focusing and one defocusing quadrupole per cell and in between we can place as many bending dipoles as needed.

*Extra: Why electron collider? - Precision colliders require leptons (elementary particle itself) to collide and not hadrons (which are "made of" many sub-particles). Therefore, providing a 175GeV energy to electrons will allow us to make better profit of that energy, i.e our measurement will be more precise.

b) Phase advance per cell: \Delta \mu = \pi/2

More advantageous for Half bend dispersion suppressor. (Advantages of such choice to be discussed in 3)

c) Cell layout
d) Bending angle of dipoles
e) Quadrupole strength
f) MAD-X implementation of the FODO Cell:
Steps: Define the sequence shown in the layout.
Match tunes to 0,25 (according to phase advance)
Match chromaticities to 0 → Need for different sextupole strength
Compare result with theoretical ones.

After having shown the pictures, one can discuss why the sextupole strength for the defocusing quadrupole is larger than for the focusing one: Since chromaticity correction depends both on dispersion and sextupole strength, since D(s) follows \beta_x behaviour, whenever D(s) is weaker a stronger sextupole strength is needed and viceversa.

h) Equilibrium emittance and energy loss:
Show formulas, values. The emittance is twice the target one: This justifies the addition of dispersion supressor sections before the straight sections in which experiments will be performed, since the smaller the dispersion is, the lower the equilibrium emittance gets.

3.- DISPERSION SUPPRESSORS AND STRAIGHT SECTIONS

a) Dispersion Suppressor Layout justification:
Choice of Half Bend Dispersion Suppressor: It’s easier to implement since one can use the same magnets he’s been using all over the machine. It’s an elegant scheme easily implemented with the selected phase advance.
Disadvantages of other models: Dipole based suppressor – affects geometry
       Quadrupole suppressor – high \beta_{x,y} → High aperture

It’s also cheaper.
Mirror symmetric scheme: The left dispersion suppressor aims to vanish the dispersion for the straight section, whereas the right one must restore it so that we recover FODO cell periodicity.

*(?) Perhaps before showing plots let clear the scheme: FODO, DSL, DSR, FODO.

b) Straight sections:
To be inserted in the 0-Dispersion area (middle of last plot). Show pictures.

c) Matching sections:
Justification: In order to preserve periodicity after inserting the new sections, we have to check that the optical functions at the end of the left dispersion suppressor match the optical functions at the straight sections. Same matching has to be verified for the end of the straight section and the beginning of the right dispersion suppressor.
Indeed, the matching section consists of n FODO cells with tunable quadrupole strengths. Since we need to match \alpha_x, \alpha_y, \beta_x, \beta_y, D_{x} and D_{px} , six degrees of freedom (I.e six quadrupoles) are needed in each side.

d) Closed structure including FODO cells and STRAIGHT sections (+ disp.sup and matches):
Perhaps show plots of the whole structure or choose ¼
* (If relevant/asked): Bastian’s guru mode: Need for parallel matching with all cells (the final objective is to match the bending FODO section optical parameters with the parameters in the straight sections. However, we’ve done the matching so far in the adjacent sections, but no check has been made on the overall matching.

Comment on total tune and total chromaticity:
Qx = 326,55 → Matches design requisite (phase advance of 90º every Lcell) + avoids resonances.
Dqx = 1 → Negative chromaticities can lead to head-tail instabilities above transition. Clearly, we are above transition since we are working with electrons (this can also be checked calculating \alpha_p = \frac{\langle D_x \rangle}{\rho} \simeq \frac{0,2}{9072} = 2,2 \cdot 10^{-5} and thus \gamma_t = \frac{1}{\sqrt{\alpha_p}} = 212,98 \ll \gamma_e ). Therefore, in order to avoid this instability, we choose a chromaticity of 1 (so that even if the system fluctuates, we are “far enough”)

4.- RF SECTIONS

U = eV_{RF} \sin{(2\pi (\phi-hf_0t))} - The energy lost due to synchrotron radiation must be compensated by the energy gain provided by the RF cavities.

a) Parameters discussion – Choice of lag phase (synchronous phase).
Because of what we’ve been told by Topic II experts, the required Vrf = 10,64 GeV. Making use of the previous formula evaluating after one turn (t = T0),
U_{turn} = eV_{RF} \sin{(2\pi(\phi - h)} = eV_{RF} \sin{2\pi\phi} \rightarrow \phi = \arcsin{\left( \frac{U_{turn}}{eV_{RF}}\right)}/(2\pi)

However, since we are above transition, stability requires the synchronous phase to be
\phi =0,5 - \arcsin{\left( \frac{U_{turn}}{eV_{RF}}\right)}/(2\pi) \simeq 0,33 rad.

b) RF Cell layout
c) Plots of the beta functions, dispersion
d) Plots of the ideal closed orbit vs toothsaw distorsion.
Explanation: x(s) = x_{\beta}(s) + D(s)\delta_p

Since we are studying the ideal particle, x_{\beta}(s)= 0 and x = D(s)\delta_p is being displayed. Given that D(s) is positive in the bendings (oscillates from 0,1 to 0,2 m), basically the deviations of the horizontal orbit with respect to 0 are due to a dp/p (or equivalently an energy gain or loss)

Therefore, the plot shows how the particle starts at x=0 and it gains energy from the rf cavity. Then, it travels along the structure, radiating thus loosing energy. When it encounters a straight section where the RF cavity is in, D(s) = 0 and therefore x = 0. Finally, after that straight section (with the RF cavity), it has gained energy and therefore it comes back to the initial amplitude.

e) Emittance:
We recover what we calculated. Perhaps, show relative deviation with previously calculated (2h).

How many particles and bunches can you fill into the ring before you reach the limit of synchrotron radiation power?